## Slide 1: Operation Clean Sweep EU
(bow-tie model user instructions for the pellet loss estimation mathematical model)
This presentation is intended to be a comprehensive user manual to set up the model quickly. For a deeper understanding of the calculus behind the model, please refer to the instructions manual.

## Slide 2: Bow-tie implementation and instructions (I)
For the use of this Bow-Tie model template, first and foremost a meticulous assessment of the plant and reading of the guidance must be carried out
The bow-tie model for reporting purposes contains a completely automated procedure for data input and calculation
The extension of the model is adapted according to the user’s input (macros developed)
A full set of instructions (with screenshots and explanation) has been compiled in the “BowTie Template Instructions”
Several examples were also created in the BowTie Model package

## Slide 3: OCS | Mathematical Model
BOW-TIE MODEL
This model is designed to estimate the plastic pellet spills and losses that occur at a production site. The task is challenging due to the lack of input data and the degree of uncertainties present. However, the model is intended to be easy to comprehend and implement, and of low complexity.
The model's name derives from the scheme below, where it is shown that the model starts from the spill sources and ends with the losses. In between, there are preventive barriers and mitigation barriers, while all the material that surpasses the preventive barriers constitutes spills
SPILL SOURCES
LOSS
PREVENTIVE BARRIERS
MITIGATING BARRIERS
SPILL

## Slide 4: OCS | Mathematical Model
ACRONYMS
The following acronyms will be displayed throughout the model, along with their definitions:

## Slide 5: OCS | Mathematical Model
BOW-TIE MODEL
The data to feed the model must be available. For that purpose, a series of steps should be followed to ensure the proper function of the Bow-Tie model.
The Bow-Tie model is embedded in an MS Excel® workbook. The main worksheet is Instructions, which includes a list with the instructions to follow for the completion of the model and a table with the description of all the variables and parameters involved, as well as some acronyms; Structure, which the structure of the model is adjusted; Inputs, where all the measurements/estimations need to be charged; CPi and MAi, where the structure of the preventive/mitigating barriers is defined; and Analysis, where a summary of the Macro Areas and plant performance takes place. The remaining worksheet only contains some functional reference tables, but they do not require any input from the user nor show any result.

## Slide 6: OCS | Mathematical Model
BOW-TIE MODEL
The model inputs can be sorted into two general categories: measurement inputs and model structure/parameters. The first one is the set of measurements obtained from the plant, and the second changes the way in which the model is structured and the information is processed; i.e., the disposition of the Critical Points and Macro Areas, the preventive and mitigating barriers, as well as the evaluation of the efficiency of each barrier.
The measurement inputs only require the quantity of the Spill without Barrier [Kg/time] and the Throughput Measurement [Kg/time] – i.e., the streaming throughput of material at the measurement point – of the processed material at that specific critical point/macro area. In case the spills without a barrier are known to be in between a value range, it is advised to only use the maximum value, as this corresponds to a worst-case scenario. For each of these measurements, the sampling time frame can be adjusted separately, and then the amount of the measurement will be annualized automatically.
measurement/estimation inputs
BOW-TIE MODEL
outputs
model structure/parameters

## Slide 7: Bow-Tie Model
BOW-TIE MODEL
BOW-TIE APPROACH FOR RISK REDUCTION PURPOSE:
Assess risk reduction magnitude/potential
BOW-TIE APPROACH FOR REPORTING PURPOSE:
Estimate losses to the environment

## Slide 8: OCS | Mathematical Model
BOW-TIE MODEL
The other class of inputs is regarding the structure of the model. There are spreadsheets assigned to each Macro Area. In case a CP-approach is followed, there are spreadsheets under the name CP1, CP2, …, CPn; where the information must be filled in. Elseways, in the case of an MA-approach, the spreadsheets to fill are under the names MA1, MA2, …, MAn.
In the CP/MA spreadsheets, the preventive and mitigating barriers must be selected. These barriers can be placed in series or parallel disposition, accordingly as they are disposed of in the plant.
In the first worksheet, Instructions, the following list of instructions is found. Each of the numbers associated with each step is also placed throughout the document to show where that action must take place. Moreover, next to each number there is a reference to the worksheet where the action is required.

## Slide 9: OCS | Mathematical Model (STEPS)

## Slide 10: OCS | Mathematical Model (STEPS)
STEPS 1-3
First, the structure of the model needs to be adapted to every particular case. In the worksheet Structure – following the numbered steps 1-3; the number of Macro Areas must be defined, and after that, the type of approach, and the number of Critical Points per Macro Area – only applicable in the CP-approach, not with the MA-approach. Once this data is charged, press the START MODEL button.
This operation reduces and adjusts the whole structure of the model to the plant in question, and enables a series of tables to place further data.
The button FULL STRUCTURE shows the entire model without restrictions; and the button CLEAR DATA not only executes the same functions as FULL STRUCTURE but also clears all inputs. Nonetheless, in normal use of the Bow-Tie model, the buttons to be used are START STRUCTURE and RESET STRUCTURE.

## Slide 11: OCS | Mathematical Model (STEPS)
Figure. Capture from worksheet Structure.
STEPS 1-3

## Slide 12: OCS | Mathematical Model (STEPS)
STEPS 4-7
In the worksheet Inputs, steps 4-6 must be followed. For step 4, the value for the total annual Throughput of the Plant must be charged. Afterwards, for steps 5-6, the Macro Area and each one of its critical points – only in the case of the CP-approach – must be defined from a deployable list.
In case the necessary options are not included, the user can just overwrite the desired name on these cells.
Figure. Captures from worksheet Inputs. Macro Area and critical points definition.

## Slide 13: OCS | Mathematical Model (STEPS)
STEPS 4-7
In the next step, the values for Time, Spill without Barrier, and Throughput Measurement must be provided in each Macro Area. Notice that the cells that require an input, initially show a hyphen, “-”. The remaining factors in the table are calculated automatically; i.e., Throughput Annual (AT), Annual Spill (AS), and SP.
Figure. Capture from worksheet Inputs. Spills quantities and probabilities.

## Slide 14: OCS | Mathematical Model (STEPS)
STEPS 8-10
These steps take place in each one of the worksheets concerning each of the Macro Areas. Depending on whether a certain Macro Area will be approached with the CP approach or the MA approach, the corresponding worksheet will be named CP# or MA#, respectively. In these worksheets, the key element is the definition of the preventive and mitigating barriers. For the first ones, these can be placed one after the other in series, or they can be in parallel chains of barriers, according to the specifications made in the worksheet Structure. For each barrier, there is a table like this one:
The top of the table deploys a list where the barrier is set up; if the desired name is not found, the cell can be simply overwritten by any type of entry name.
Figure. Capture from the worksheet CP# or MA#. Table to define a preventive/mitigating barrier.

## Slide 15: OCS | Mathematical Model (STEPS)
STEPS 8-10
Thereafter, once the barriers are in place, a series of coefficients must be defined regarding their properties, providing a quick assessment of the dependability and performance capability of the barrier. The parameters in question are, in the case of dependability (D), reliability (R), and availability (A); and for the performance capacity, effectiveness (E), and independence (I), respectively. For each one of these parameters, a set of coefficients {1,2,3} are available. The criteria to be followed in assigning each of these parameters are:
Reliability (R) measures the failure rate of a barrier to perform its intended task. This can be classified as the total number of failures divided by the total uptime of the barrier. 1 = below 89%; 2 = 89-99%; 3 = above 99%.
Availability (A) measures the total uptime of the barrier divided by total downtime to get the percentage of available functional hours [MTBR / (MTBR + MTTR) (hours)]. 1 = below 89%; 2 = 89-99%; 3 = above 99%.
Effectiveness (E) defines the ability of a barrier to avoid pellets spilled or lost passing through it. Hardware; i.e., filters; can be defined by the product specification; i.e., filter efficiency. The effectiveness is given a score of 1 when below 70%, a score of 2 when comprised between 70 and 90 %, and a score of 3 when above 90%. 1 = below 70%; 2 = 70-90%; 3 = above 90%.
Independency (I) defines the promptness and the certainty of the barrier intervention: 1 – manually activated and executed; 2 – manually activated, automatically executed; 3 – automatically activated and executed.

## Slide 16: OCS | Mathematical Model (STEPS)
STEPS 8-10
The effectiveness of a barrier is determined by two main factors: Dependability and Performance Capability. Dependability is determined by the barrier’s Reliability and Availability, each of which is assigned a score in the range [1-3]. The scores are then used to determine the degree of Dependability. On the other hand, Performance Capability relies on the Effectiveness and Independence of a barrier. Based on the scores assigned to these latter factors, the Performance degree is determined.

## Slide 17: OCS | Mathematical Model (STEPS)
STEPS 8-10
The overall efficiency of a barrier is determined by taking into account two factors: Dependability and Performance Capability. These factors are correlated with each other and depend on whether the barrier is preventive or mitigating.
Then, a series of calculations are executed based on the information provided. This includes the Spill after Barriers (SB), the Spill Probability after Barriers (SPB), and after them, a Reduction Factor label is calculated as an evaluation score for the set of preventive barriers put in place.
At this point, the last input demanded by the model is the Main MA Factor, which determines the fraction of spills that occur in the main parts of the Macro Area, making the distinction from the Peripheric Areas (PA). Once the spills are split into their respective area, the mitigation barriers must be defined, with their respective parameters. After that, the Loss of pellets, Loss Probability (LP), and an MA reduction factor are obtained.

## Slide 18: OCS | Mathematical Model (STEPS)
RESULTS
In the worksheet of each Macro Area, after the mitigating barriers, their evaluation and the estimated losses are displayed. Here, the Loss Probability (LP) and LOSS – both expressing a minimum and maximum estimation and Macro Area reduction factor after preventive and mitigating barriers are displayed.

## Slide 19: OCS | Mathematical Model (STEPS)
RESULTS
Besides these partial results in each Macro Area, the main results are condensed in tables located in the worksheet Inputs, next to the values provided for the spills. If the CP-approach is followed, results appear as SB and LOSS; otherwise, if the MA approach is followed, results appear as SB* and LOSS*.
Lastly, all the results for all the Macro Areas are condensed in the worksheet Analysis. These tables include a summary of the most important estimations the model provides, i.e., the annual spills (AS) per Macro Area, the Spill Probability after Barriers (SPB), the Loss Probability (LP), and the Spills after Barriers (SB). Moreover, the last table calculates the most important factors to evaluate the performance of the whole plant in relation to the pellet losses, as is the case with the relationship between the total spills and the throughput of the plant (AS / T) and the total amount of pellet loss per unit of throughput (LOSS / T).

## Slide 20: OCS | Mathematical Model (STEPS)
RESULTS
Figure. Capture from worksheet Analysis.

## Slide 21: OCS | Mathematical Model (approaches to reporting)
APPROACHES TO REPORTING (decision-making three)
Depending on the information available, the user must decide which version of the model to use. The most important part of the inputs is the information about the quantity of spills or material collected at the barriers. This information is going to be crucial at the time of choosing a model. The four possibilities for spills quantities information are: the Annual Spills, the Collected material at Preventive Barriers (CPB), the Collected material at Mitigating Barriers (CMB), and the Disposed and Recycled material (DR).
In all the cases, the mitigation barriers are required to be fully defined and in place, no matter the model version, these barriers are a key component of the model and must be defined for each of the macro areas.
For the case that the inputs are the Annual Spills, the preventive barriers must be totally defined, and the Risk Assessment Model is the choice to follow. For the Collected material at PB, it is also required to provide an average efficiency of this set of barriers in each macro area, and the Reporting Model Case I is the corresponding choice. For the case of Collected material at Mitigating Barriers (CMB), the choice is the Reporting Model Case II. Lastly, if the input data is the Disposed and Recycled material (DR), the version to use is the Reporting Model Case III.

## Slide 22: OCS | Mathematical Model (approaches to reporting)
APPROACHES TO REPORTING (decision-making three)

## Slide 23: Evaluating operating losses: approaches based on available input data/plant layout (1/3)
Tiered approach:
Approaches 1-3 – simplified input – worst case estimates
Starting point | Tier
Approach 1: Pellets sent to recycling/waste management | 1
Approach 2: Pellets collected in mitigating barriers | 1
Approach 3: Pellets collected in preventive barriers | 1,5
Approach 4: full risk assessment | 2

## Slide 24: Evaluating operating losses : approaches based on available input data/plant layout (2/3)
Starting point | Information needed | Relevant parameters | Field of applicability/limitations
Approach 1: Pellets sent to recycling/waste management | Quantity of pellets sent to recyclers and/or waste management companies | Quantity of collected material sent to recycling and/or waste management+ efficiency of mitigating barriers | -Mostly for «closed systems» (limited preventive barriers needed) Not applicable if the macroplastic waste generated cannot be differentiated from microplastics Typical example: resin production
Approach 2: Pellets collected in mitigating barriers | Quantity of pellets collected in the mitigating barriers | Quantity of pellets collected in the mitigating barriers+ efficiency of mitigating barriers | First quantitative scoping disadvantage: gets focus away from preventive barriers Well suited however with first implementation more applicable to converters
Tier 1
Tier 1

## Slide 25: Evaluating operating losses : approaches based on available input data/plant layout (3/3)
Starting point | Information needed | Relevant parameters | Field of applicability/limitations
Approach 3: Pellets collected in preventive barriers | Quantity of pellets collected in the preventive barriers and a generic efficiency factor for the latter | CPB + average efficiency of preventive barriers+ efficiency of mitigating barriers | This approach considers spills collected in preventive barrier in a more holistic way (default realistic worst case efficiencies). This means that it is mainly applicable when preventive barriers have already been implemented in all the plant macro-areas. Not applicable to closed systems.
Approach 4: same as risk reduction | Detailed info on barrier efficiency, estimated and/or measured pellets in barriers | Same as risk reduction | A refined model for risk minimisation. Applicable to plant with a lot of ressources and at a further implementation stage after the first risk identified by risk mapping has been addressed.
Tier 1,5
Tier 2

## Slide 26: OCS | Mathematical Model (STEPS)
CASE EXAMPLE (worksheet Structure)
MAs NUMBER
CPs NUMBER AND APPROAH TYPE

## Slide 27: OCS | Mathematical Model (STEPS)
MACRO AREA RESULTS
SPILLS INPUT
DEFINITION OF MA AND CPs
TOTAL THROUGHPUT
CASE EXAMPLE (worksheet Inputs)

## Slide 28: OCS | Mathematical Model (STEPS)
CASE EXAMPLE
Figure 1. Pellet spills and loss – Plant Material Flow Diagram (example)
CRITICAL POINTS
PREVENTIVE BARRIERS
PELLETS SPILL
MITIGATING BARRIERS
PELLETS LOSS
BARRIERS SIZE
CASE EXAMPLE (worksheet CP#)

## Slide 29: OCS | Mathematical Model (STEPS)
CRITICAL POINTS
PREVENTIVE BARRIERS
BARRIERS SIZE
PELLETS SPILL
MITIGATING BARRIERS
PELLETS LOSS
CASE EXAMPLE (worksheet MA#)